## Slide 1: Machine Learning on Tiny Hardware
Robert Bayer, PhD Fellow @ ITU
CCIT Symposium
Dec. 11, 2023, Copenhagen
roba@itu.dk
RAD
dasya.itu.dk
rad.itu.dk

## Slide 2
Increased privacy / regulations
Real-time systems
Low bandwidth
Saves energy and compute!
Why Tiny/EdgeML?

## Slide 3
Example Use Case – Satellites!
Small Earth-observation satellites
Very low network bandwidth
Produces large amount of data
DISCO 1&2

## Slide 4
Machine Learning on Satellites
Challenges
Low power budget (2 W avg, 5 W max)
Low latency requirements (4.42 s / image)
Need for robustness and flexibility
NVIDIA RTX 4060 115W TDP
Source: NVIDIA
4512px
4512px

## Slide 5
TinyML Hardware Landscape
Microcontrollers / CPUs​
+ Low power footprint​
- Low degree of specialization​
- Low degree of parallelism ​
Edge SoCs + GPUs​
+ High degree of parallelism​
- High power footprint​
ASICs​
+ High degree of specialization​
+ High degree of parallelism​

## Slide 6
Looking for the Best Candidate
Chart: Per-image inference latency (s)
| ARM Cortex | Jetson Nano | NCS2 | CoralAI Micro | CoralAI Mini | CoralAI USB
DM=0.25 | 118.8 | 1.956 | 3.19 | 4.88 | 3.902 | 3.319
DM=0.5 | 3.206 | 3.137 | 5.196 | 4.118 | 3.514
DM=1 | 8.176 | 4.539 | 6.031 | 4.667 | 4.012
budget | 4.42 | 4.42 | 4.42 | 4.42 | 4.42 | 4.42
Chart: Per-image inference power consumption (mWh)
| ARM Cortex | Jetson Nano | NCS2 | CoralAI Micro | CoralAI Mini | CoralAI USB
DM=0.25 | 12.1 | 2.99 | 3.3 | 1.36 | 1.3 | 2.22
DM=0.5 | 4.97 | 3.48 | 1.36 | 1.43 | 2.44
DM=1 | 11.63 | 5.44 | 1.819 | 1.82 | 2.93
Low power draw ≠ high efficiency
Highest degree of specialization necessary

## Slide 7
Designed image processing unit based on CoralAI Dev Board Mini
DISCO 1 launched in April 2023
Currently working on DISCO 2
Results

## Slide 8
Current & Future Research
Need for standardized benchmarking
Would save us a lot of time
Standardized benchmarks too small or too big
Resource management
Co-location of multiple tasks
Task placement

## Slide 9
Thank you!
Q&A